## Slide 1
Direct construction of stellarator shapes with good confinement
J Plasma Phys 84, 905840616 (2018) J Plasma Phys 85, 905850103 (2019) PPCF 61, 075001 (2019) arXiv:1909.08919 arXiv:1908.10253 github.com/landreman/quasisymmetry
Matt Landreman1, Wrick Sengupta2, Gabe Plunk3 , Per Helander3 1. University of Maryland 2. NYU 3. IPP

## Slide 2
Advantages of stellarators: steady-state, no disruptions, no power recirculated for current drive, no Greenwald limit, don’t rely on plasma for confinement.

## Slide 3
Advantages of stellarators: steady-state, no disruptions, no power recirculated for current drive, no Greenwald limit, don’t rely on plasma for confinement.
But, alpha losses & neoclassical transport would be too large unless you carefully choose the geometry.

## Slide 4
Advantages of stellarators: steady-state, no disruptions, no power recirculated for current drive, no Greenwald limit, don’t rely on plasma for confinement.
But, alpha losses & neoclassical transport would be too large unless you carefully choose the geometry.
A solution: quasisymmetry
Boozer angles
Guiding-center Lagrangian in Boozer coordinates depends on (𝜃,𝜁) only through B=|B|.

## Slide 5
Boozer angles
(Or, weaker conditions like omnigenity)
Advantages of stellarators: steady-state, no disruptions, no power recirculated for current drive, no Greenwald limit, don’t rely on plasma for confinement.
But, alpha losses & neoclassical transport would be too large unless you carefully choose the geometry.
A solution: quasisymmetry

## Slide 6
Boozer angles
(Or, weaker conditions like omnigenity)
Advantages of stellarators: steady-state, no disruptions, no power recirculated for current drive, no Greenwald limit, don’t rely on plasma for confinement.
But, alpha losses & neoclassical transport would be too large unless you carefully choose the geometry.
A solution: quasisymmetry
How do you find MHD equilibria with these properties?

## Slide 7: The conventional approach to finding quasisymmetric fields works but has shortcomings
Want magnetic field strength B to have quasisymmetry:

## Slide 8: The conventional approach to finding quasisymmetric fields works but has shortcomings
Want magnetic field strength B to have quasisymmetry:

## Slide 9: The conventional approach to finding quasisymmetric fields works but has shortcomings
Want magnetic field strength B to have quasisymmetry:
Computationally expensive.
What is the size & character of the solution space?
Result depends on initial condition, so cannot be sure you’ve found all solutions.

## Slide 10: Expansion about the magnetic axis can be a powerful practical tool for generating quasisymmetric & omnigenous stellarators
Accurate at least in the core of any configuration.
Hasn’t been considered much since numerical optimization began in ~1980s.

## Slide 11: Expansion about the magnetic axis can be a powerful practical tool for generating quasisymmetric & omnigenous stellarators
Accurate at least in the core of any configuration.
Hasn’t been considered much since numerical optimization began in ~1980s.
Complements the traditional optimization approach:
  Many orders of magnitude faster.
  You can parameterize all possible solutions.
  Can generate new initial conditions that can be refined by optimization.

## Slide 12: Outline
Theory for O(r) quasisymmetry
Comparison to optimized configurations
The landscape of solutions
O(r) omnigenity
O(r2) quasisymmetry

## Slide 13: Outline
Theory for O(r) quasisymmetry
Comparison to optimized configurations
The landscape of solutions
O(r) omnigenity
O(r2) quasisymmetry

## Slide 14: Garren & Boozer (1991): Write position vector x using axis’s Frenet frame, expand in small r

## Slide 15: Garren & Boozer (1991): Write position vector x using axis’s Frenet frame, expand in small r
Same for Y & Z.

## Slide 16
Same for Y & Z.
Garren & Boozer (1991): Write position vector x using axis’s Frenet frame, expand in small r

## Slide 17
Garren & Boozer (1991): Write position vector x using axis’s Frenet frame, expand in small r
Same for Y & Z.

## Slide 18
Garren & Boozer (1991): Write position vector x using axis’s Frenet frame, expand in small r
Same for Y & Z.

## Slide 19: Garren & Boozer’s equations yield a practical algorithm
Inputs:
Shape of the magnetic axis, with 𝜅 ≠ 0. (Determines QA vs QH.)
3 real numbers:
  I2: Current density on the axis. (Usually 0).
  𝜎(0): Rotation of the elliptical flux surfaces at toroidal angle=0.
  , which controls elongation and field strength:
(Pressure doesn’t matter to this order.)

## Slide 20: Garren & Boozer’s equations yield a practical algorithm
Inputs:
Shape of the magnetic axis, with 𝜅 ≠ 0. (Determines QA vs QH.)
3 real numbers:
  I2: Current density on the axis. (Usually 0).
  𝜎(0): Rotation of the elliptical flux surfaces at toroidal angle=0.
  , which controls elongation and field strength:
(Pressure doesn’t matter to this order.)
Theorem: Given this data, a unique O(r) quasisymmetric solution exists.
ML, Sengupta, & Plunk, J Plasma Phys 85, 905850103 (2019)
⟹ The size of the space of configurations that are quasisymmetric to O(r) is precisely understood.

## Slide 21: Garren & Boozer’s equations yield a practical algorithm
Inputs:
Shape of the magnetic axis, with 𝜅 ≠ 0. (Determines QA vs QH.)
3 real numbers:
  I2: Current density on the axis. (Usually 0).
  𝜎(0): Rotation of the elliptical flux surfaces at toroidal angle=0.
  , which controls elongation and field strength:
(Pressure doesn’t matter to this order.)
Theorem: Given this data, a unique O(r) quasisymmetric solution exists.
Outputs:
Shape of the surfaces around the axis. (Elongation & rotation of ellipses.)
Rotational transform on axis.

## Slide 22: Example construction: quasi-axisymmetry
Inputs:
Results:
Plug in r = 0.1 m.
R [m]
Z [m]
B [T]

## Slide 23: The construction can be verified by running an MHD equilibrium code (VMEC) which does not make the expansion.
Inputs:
Results: (R/a = 10)
R [m]
Z [m]
B [T]

## Slide 24: Outline
Theory for O(r) quasisymmetry
Comparison to optimized configurations
The landscape of solutions
O(r) omnigenity
O(r2) quasisymmetry

## Slide 25: The construction can be fit to quasisymmetric stellarators designed by optimization
Adopt the same axis shape.
Fit to minimize difference in the shapes of a near-axis surface.

## Slide 26: The direct construction gives an accurate match to the on-axis rotational transform in quasisymmetric stellarators designed by optimization
NCSX
Adopt the same axis shape.
Fit to minimize difference in the shapes of a near-axis surface.

## Slide 27: The direct construction gives an accurate match to the near-axis surface shapes of quasisymmetric stellarators designed by optimization
r/a=0.1
r/a=0.2
HSX
Dotted: VMEC equilibrium
Solid: Garren-Boozer construction
Henneberg et al

## Slide 28: Outline
Theory for O(r) quasisymmetry
Comparison to optimized configurations
The landscape of solutions
O(r) omnigenity
O(r2) quasisymmetry

## Slide 29: The fast construction enables brute-force surveys of ”all” quasisymmetric fields
Rotational transform
Maximum axis curvature
Color = N = # of times B contours rotate around magnetic axis
2.4x108
configurations

## Slide 30: Brute-force searching is already yielding some new configurations
Quasi-helical symmetry with
2 field periods
1 field period

## Slide 31: Brute-force searching is already yielding some new configurations
Quasi-helical symmetry with
1 field period
2 field periods

## Slide 32: Outline
Theory for O(r) quasisymmetry
Comparison to optimized configurations
The landscape of solutions
O(r) omnigenity
O(r2) quasisymmetry

## Slide 33: The near-axis analysis can be generalized to construct omnigenous configurations
G G Plunk, ML, and P Helander, arXiv:1909.08919, Accepted in J Plasma Phys
Omnigenity:
bounce

## Slide 34: The near-axis analysis can be generalized to construct omnigenous configurations
Omnigenity:
bounce
Implications for B(r,𝜃,𝜁):
[Cary & Shasharina (1997)]
All B contours close toroidally, helically, or poloidally.
Distance along B between bounce points is the same for every field line on a flux surface.
B [T]
B [T]
✓
✘
G G Plunk, ML, and P Helander, arXiv:1909.08919, Accepted in J Plasma Phys

## Slide 35: The near-axis analysis can be generalized to construct omnigenous configurations
Omnigenity:
Garren & Boozer (1991):
bounce
Implications for B(r,𝜃,𝜁):
[Cary & Shasharina (1997)]
All B contours close toroidally, helically, or poloidally.
Distance along B between bounce points is the same for every field line on a flux surface.
for any equilibrium, not just quasisymmetry.
G G Plunk, ML, and P Helander, arXiv:1909.08919, Accepted in J Plasma Phys

## Slide 36: The near-axis analysis can be generalized to construct omnigenous configurations
Omnigenity:
Garren & Boozer (1991):
bounce
Implications for B(r,𝜃,𝜁):
[Cary & Shasharina (1997)]
All B contours close toroidally, helically, or poloidally.
Distance along B between bounce points is the same for every field line on a flux surface.
for any equilibrium, not just quasisymmetry.
(Cary & Shasharina 1997) + (Garren & Boozer 1991) = (Plunk et al 2019)
G G Plunk, ML, and P Helander, arXiv:1909.08919, Accepted in J Plasma Phys

## Slide 37: The near-axis analysis can be generalized to construct omnigenous configurations

## Slide 38: The near-axis analysis can be generalized to construct omnigenous configurations

## Slide 39: Outline
Theory for O(r) quasisymmetry
Comparison to optimized configurations
The landscape of solutions
O(r) omnigenity
O(r2) quasisymmetry

## Slide 40: The O(r2) construction allows triangularity, Shafranov shift, and more accurate quasisymmetry.
Same for Y & Z.

## Slide 41: The O(r2) construction allows triangularity, Shafranov shift, and more accurate quasisymmetry.
3 new input parameters: p2, B2c, B2s.
Same for Y & Z.

## Slide 42: The O(r2) construction allows triangularity, Shafranov shift, and more accurate quasisymmetry.
3 new input parameters: p2, B2c, B2s.
Net loss of 1 degree of freedom. My approach: B20(𝜁) is an output. Need to adjust inputs so B20(𝜁) ≈ constant.
Same for Y & Z.

## Slide 43: The O(r2) construction allows triangularity, Shafranov shift, and more accurate quasisymmetry.
3 new input parameters: p2, B2c, B2s.
Net loss of 1 degree of freedom. My approach: B20(𝜁) is an output. Need to adjust inputs so B20(𝜁) ≈ constant.
Same for Y & Z.
Minimize X2 & Y2, to maximize the r at which surfaces begin to self-intersect.

## Slide 44: Examples of the O(r2) construction
QA
QH
𝜄 = 0.42
𝜄 = 1.14

## Slide 45: Quasisymmetry expected for the O(r2) construction is confirmed by VMEC.
QA
QH

## Slide 46: We can now numerically demonstrate Garren & Boozer’s scaling: Bnonsymm ~ 1/A3
QA
QH

## Slide 47: We can now numerically demonstrate Garren & Boozer’s scaling: Bnonsymm ~ 1/A3
QA
QH
!

## Slide 48: Quasisymmetry can be achieved to any desired precision, e.g. Bnonsymm ≤ BEarth

## Slide 49: Future work
Higher order: Calculate B3 so symmetry-breaking can be minimized.
Examine MHD & gyrokinetic stability using the expansion.
Can anything be proved about the number or character of O(r2) solutions?
Is there an analogous construction to give quasisymmetry at an off-axis surface?
Check coil feasibility for newly discovered configurations.

## Slide 50: Conclusions
The near-axis expansion enables transport-optimized stellarator configurations to be generated orders of magnitude faster than before.
We precisely understand the size of the space of magnetic fields that are quasisymmetric near the axis (to O(r)).
There is hope of definitively identifying all regions of parameter space with practical quasisymmetric fields (near the axis).
J Plasma Phys 84, 905840616 (2018) J Plasma Phys 85, 905850103 (2019) PPCF 61, 075001 (2019) arXiv:1909.08919 arXiv:1908.10253 github.com/landreman/quasisymmetry

## Slide 51: Conclusions
The near-axis expansion enables transport-optimized stellarator configurations to be generated orders of magnitude faster than before.
We precisely understand the size of the space of magnetic fields that are quasisymmetric near the axis (to O(r)).
There is hope of definitively identifying all regions of parameter space with practical quasisymmetric fields (near the axis).
We might discover qualitatively new magnetic configurations for fusion?
J Plasma Phys 84, 905840616 (2018) J Plasma Phys 85, 905850103 (2019) PPCF 61, 075001 (2019) arXiv:1909.08919 arXiv:1908.10253 github.com/landreman/quasisymmetry

## Slide 52: Extra slides

## Slide 53: Expansion about the magnetic axis can be a powerful practical tool for generating quasisymmetric & omnigenous stellarators
Complements the traditional optimization approach:
Many orders of magnitude faster.
You can parameterize all possible solutions.
Can generate initial conditions that can be refined by optimization.

## Slide 54: We now have a recipe for generating quasisymmetric VMEC input files: Set r to a small finite value a.
Inputs:
Results:

## Slide 55: We now have a recipe for generating quasisymmetric VMEC input files: Set r to a small finite value a.
Inputs:
Results:

## Slide 56: The construction can be verified by comparing to VMEC + BOOZ_XFORM.
Inputs:
Results:

## Slide 57: Alternative method to generate a finite-thickness boundary: find coils to make a skinny surface, then see what you get outside.

## Slide 58: Alternative method to generate a finite-thickness boundary: find coils to make a skinny surface, then see what you get outside.

## Slide 59: Quasi-axisymmetry vs quasi-helical symmetry is determined purely by the axis shape
So B contours rotate about axis with the same topology as n.

## Slide 60: Quasi-axisymmetry vs quasi-helical symmetry is determined purely by the axis shape
n does not rotate about the axis as you follow the axis around.
n rotates about the axis 4 times as you follow the axis around.
n
So B contours rotate about axis with the same topology as n.

## Slide 61: The fast construction enables brute-force surveys of ”all” quasisymmetric fields
Rotational transform
Maximum axis curvature
Color = # of times B contours rotate around magnetic axis
2.4x108
configurations

## Slide 62: The fast construction enables brute-force surveys of ”all” quasisymmetric fields
Rotational transform
Maximum axis curvature
Color = nfp (discrete rotational symmetry)
4x106
configurations
Quasi-axisymmetric solutions only

## Slide 63: The construction enables fast scans over parameter space.
274,560 solutions generated in <30s on a laptop.
Quasi-axisymmetry
Quasi-helical symmetry

## Slide 64: All stellarators built to date have ‘stellarator symmetry’, which is unrelated to quasisymmetry
Sugama et al (2011)

## Slide 65: You can make a quasi-axisymmetric stellarator without stellarator symmetry
Inputs:
Results: (R/a = 10)

## Slide 66: You can make a quasi-axisymmetric stellarator without stellarator symmetry
Inputs:
Results: (R/a = 10)

## Slide 67: We will expand in the skinniness of the inner flux surfaces
Flux surface

## Slide 68: Theory: Expand position vector using Frenet frame, equate 2 representations of B.

## Slide 69: Theory: Write position vector using Frenet frame

## Slide 70: Theory: Write position vector using Frenet frame, expand in small r = (flux)1/2

## Slide 71: Theory: Write position vector using Frenet frame, expand in small r = (flux)1/2

## Slide 72
Theory: Expand position vector using Frenet frame, equate 2 representations of B.

## Slide 73
Theory: Expand position vector using Frenet frame, equate 2 representations of B.

## Slide 74
Theory: Expand position vector using Frenet frame, equate 2 representations of B.

## Slide 75
Theory: Expand position vector using Frenet frame, equate 2 representations of B.

## Slide 76: The rotational transform computed by VMEC converges to the value computed by the Garren-Boozer approach.

## Slide 77: The ODE is solved with spectral accuracy using pseudospectral discretization + Newton iteration

## Slide 78: Of 10 configurations examined, the fit is less good for 2
ARIES-CS
CFQS
Dotted: VMEC equilibrium
Solid: Garren-Boozer construction

## Slide 79: The configurations with relatively poor fits can be explained by their larger symmetry-breaking

## Slide 80: The conventional approach to finding quasisymmetric fields works but has shortcomings
Want magnetic field strength B to have quasisymmetry:

## Slide 81: The conventional approach to finding quasisymmetric fields works but has shortcomings
Want magnetic field strength B to have quasisymmetry:

## Slide 82: The conventional approach to finding quasisymmetric fields works but has shortcomings
Want magnetic field strength B to have quasisymmetry:
Computationally expensive.
What is the size & character of the solution space?
Result depends on initial condition, so cannot be sure you’ve found all solutions.

## Slide 83: Alternative: expand equations near the magnetic axis
Magnetic axis
Mercier (1964), Lortz & Nührenberg (1976), Garren & Boozer (1991)
Magnetic field lines
Flux surfaces

## Slide 84: A key ingredient of the theory is the Frenet frame of the magnetic axis
Mercier (1964), Solovev & Shafranov (1970), Lortz & Nührenberg (1976), Garren & Boozer (1991)

## Slide 85: A key ingredient of the theory is the Frenet frame of the magnetic axis
Mercier (1964), Solovev & Shafranov (1970), Lortz & Nührenberg (1976), Garren & Boozer (1991)

## Slide 86: Garren & Boozer (1991): Write position vector x using axis’s Frenet frame, expand in small r

## Slide 87: The size of the space of fields that are quasisymmetric to O(r) can be precisely understood.

## Slide 88: The size of the space of fields that are quasisymmetric to O(r) can be precisely understood.
Theorem: A solution exists and it is unique.
ML, Sengupta, and Plunk (2019). Probably an earlier reference?

## Slide 89: The size of the space of fields that are quasisymmetric to O(r) can be precisely understood.
Theorem: A solution exists and it is unique.

## Slide 90: The symmetry-breaking Fourier amplitudes scale as predicted.

## Slide 91: Quasi-helically symmetric configurations
r/a=0.1
r/a=0.2
HSX
L-P Ku (2011)
Dotted: VMEC equilibrium
Solid: Garren-Boozer construction

## Slide 92: Quasi-axisymmetric configurations
NCSX
ESTELL
Dotted: VMEC equilibrium
Solid: Garren-Boozer construction

## Slide 93: Omnigenity is a weaker confinement condition than quasisymmetry.
Definition of omnigenity: The radial drift has a time average of 0 for all particles.
J Cary & S Shasharina, Physics of Plasmas 4, 3323 (1997).
J Cary & S Shasharina, Physical Review Letters 78, 674 (1997).
P Helander & J Nührenberg, Plasma Physics and Controlled Fusion 51, 055004 (2009).
M Landreman & P J Catto, Physics of Plasmas 19, 056103 (2012).

## Slide 94: Omnigenity is a weaker confinement condition than quasisymmetry.
Generalized
quasi-axisymmetry
Generalized quasi-poloidal
symmetry
Generalized quasi-helical
symmetry
𝜁
𝜃
𝜁
𝜁
Definition of omnigenity: The radial drift has a time average of 0 for all particles.
|B|

## Slide 95: The near-axis analysis can be generalized to construct omnigenous configurations
G G Plunk, ML, and P Helander,
In preparation
Quasi-poloidal symmetry is not possible near the axis, but omnigenity is.

## Slide 96: Outline
Construction for O(r) quasisymmetry
  Theory, & the number of solutions
  Numerical results
  Comparison to “real experiments”
  The landscape of solutions
Extensions
  Omnigenity
  O(r2) quasisymmetry

## Slide 97: Extending the construction to higher order is tricky
We can only “half-specify” the axis shape:
  A curve like the axis is given by 2 functions, e.g. {curvature, torsion} or {R(𝝓), Z(𝝓)}.
  At O(r), (# unknowns)-(# equations)=2 so we can specify (almost) any axis. But at O(r2), (# unknowns)-(# equations)=1 so we cannot.

## Slide 98: Extending the construction to higher order is tricky
We can only “half-specify” the axis shape:
  A curve like the axis is given by 2 functions, e.g. {curvature, torsion} or {R(𝝓), Z(𝝓)}.
  At O(r), (# unknowns)-(# equations)=2 so we can specify (almost) any axis. But at O(r2), (# unknowns)-(# equations)=1 so we cannot.
No existence & uniqueness theorem for solutions (yet).
Magnetic shear (variation of rotational transform) does not appear until O(r3).

## Slide 99: We are working to extend the construction to O(r2), enabling greater shaping
Const 𝜃Boozer curves
Axisymmetric
example:
Requested
Achieved
Requested
Achieved

## Slide 100: We now have a recipe for generating quasisymmetric VMEC input files: Set r to a small finite value a.
Inputs:
Results:

## Slide 101: The construction can be verified by comparing to VMEC + BOOZ_XFORM.
Inputs:
Results: (R/a = 40)

## Slide 102: The fast construction enables brute-force surveys of ”all” quasisymmetric fields
Rotational transform
Maximum axis curvature
Color = # of times B contours rotate around magnetic axis
2.4x108
configurations

## Slide 103: The fast construction enables brute-force surveys of ”all” quasisymmetric fields
Rotational transform
Maximum axis curvature
Color = # of times B contours rotate around magnetic axis
2.4x108
configurations

## Slide 104
Quasisymmetric experiments to date actually have significant departures from symmetry.

## Slide 105: Example of the O(r2) construction
Inputs:

## Slide 106: Example of the O(r2) construction
Inputs:
Results:

## Slide 107: The O(r2) construction allows triangularity and more accurate quasisymmetry.
3 new input parameters: p2, B2c, B2s.
Net loss of 1 degree of freedom. My approach: B20(𝜁) is an output. Need to adjust inputs so B20(𝜁) ≈ constant.
Shafranov shift appears at this order. Matches textbook tokamak result (e.g. Wesson, Hazeltine & Meiss):
Same for Y & Z.

## Slide 109: Garren & Boozer (1991): Write position vector x using axis’s Frenet frame, expand in small r
Results for quasisymmetry through O(r):

## Slide 110: The size of the space of fields that are quasisymmetric to O(r) can be precisely understood.
Inputs:
Shape of the magnetic axis. (Determines QA vs QH.)
3 real numbers:
  I2: Current density on the axis. (Usually 0).
  𝜎(0): Rotation of the elliptical flux surfaces at toroidal angle=0.
  , which controls elongation and field strength:
(Pressure doesn’t matter to this order.)
Theorem: Given this data, a quasisymmetric solution exists, & it is unique.

## Slide 111: Conclusions
The equations for quasisymmetric magnetic fields can be solved directly and rapidly if you expand about the magnetic axis.
The resulting construction can be useful for generating new initial conditions for optimization.
We precisely understand the size of the space of magnetic fields that are quasisymmetric near the axis (to O(r)).
There is hope of definitively identifying all regions of parameter space with practical quasisymmetric fields (near the axis).
We can discover qualitatively new magnetic configurations for fusion.
J Plasma Phys 84, 905840616 (2018) J Plasma Phys 85, 905850103 (2019) PPCF 61, 075001 (2019) arXiv:1909.08919 arXiv:1908.10253 github.com/landreman/quasisymmetry

## Slide 112: Parameter space (independent variables)
Coil shapes: arbitrary 3D curves
Coil currents
Input parameters of the Garren-Boozer near-axis quasisymmetry equations:
  Shape of magnetic axis (independent from the axis actually produced by coils!)

## Slide 113: Objective function
Differentiate Biot-Savart law

## Slide 114: Combined coil + quasisymmetry optimization using analytic derivatives successfully achieves flux surfaces & QA
Combined optimization takes < 1 hour * 1 cpu in Matlab prototype code. Could surely be accelerated.
Good vacuum surfaces out to A=1.96
Good quasisymmetry in core